PC Proxy Tracer Analysis
Peter Mills
2011-5-20

---
1. Preliminaries
Tangent model
Singular vectors and Lyapunov exponents
Outline
2. Tracer Correlation
Traditional proxy analysis
Correlation with PCs
Lyapunov spectrum
3. PC Proxy
Description
Simulation results
4. Conclusion
Summary
Outlook
References

---
1. Preliminaries
Tangent model
Consider a system of ODEs:
{d vec x} over {d t} = vec f(vec x,~ t)
Linearize this about x:
{d} over {dt}(x + %delta x) approx vec f + nabla vec f cdot %delta vec x

---
Tangent model
{"d"} over {"d" t} %delta x approx nabla vec f cdot %delta vec x
Define H such that:
"d" over {"d" t} H = nabla vec f cdot H
H(t=0)=I

---
Singular vectors
(also called principal components (PCs) or empirical orthogonal functions (EOFs))
Decompose H as follows:
H = U cdot S cdot V^T
V^T cdot V = I
U^T = U^{-1}
U is an orthonormal matrix of “right” singular vectors
V is an orthonormal matrix “left” singular vectors
S is a diagonal matrix of singular values
(Tang et al. 2006, Press et al. 1992)

---
Lyapunov exponents
The time averages of the singular values are the Lyapunov exponents:
%lambda_i = lim csub {t rightarrow infty} {1 over {2 t} log s_i}
%lambda_{i-1} le %lambda_i
If l1 is greater than zero, the system is said to be chaotic
For most systems:
lline %delta vec x rline approx lline %delta vec x(0) rline exp(%lambda_1)
(Ott 1993)

---
Singular vectors
An Eulerian tracer simulation is linear
(the tangent vector is simply the dynamics)
vec q(t_i) approx H_i cdot vec q(0)
H_N = A_N cdot A_{N-1} cdot ~...~~cdot A_2 cdot A_1
Where
q(0) is the initial tracer field
q(tN) is the final tracer field
A_i approx I + %DELTA t_i nabla vec f divides_{t=t_i,~vec q=vec q(t_i)} ~

---
2. Tracer correlation
Two different tracers integrated over a long time with the same wind fields will become correlated
Can be used to infer global fields of long-lived tracers (such as O3) based on only a few sparse measurements
(Randall et al. 2002, Allen & Nakamura 1999)

---
Tracer correlation: extreme example
Zonally symmetric versus meridionally symmetric initial field
Date
R

---
Correlation with first principal component
Date
R

---
Lyapunov spectrum
Date
Singular value

---
Principal Component Proxy
Description
Generate matrices A1, A2, A3...
Find the left singular vectors of Hj for lead time, j
Generate right singular vectors from {Ai}
Correlate measurements with right singular vectors
**note: we use only a small subset of singular vectors with largest associated singular values

---
PC proxy description
sum from{i=1} to m c_i vec w_k cdot H_k cdot vec v_i = q_k
Where:
qk is the measured tracer value at lead time k
Hk is the matrix mapping for lead time k
vi is the ith singular vector
wk is a vector of interpolation coefficients
ci is a fitted coefficient
**note: H is nxn where n is the number of grid points in the simulation; meanwhile, m<<n

---
Simulation results
Used top 5 singular vectors at a lead time of 2 months
Chose 10 random points over 1 day period at approximate lead time
Interpolated tracer values at these points from zonally-symmetric-initialized tracer
Performed PC proxy using these values

---
Simulation: original versus reconstructed
Date
R

---
Conclusions
Summary
Based on the tracer dynamics, PC proxy analysis was able to reconstitute a simulated passive tracer to high accuracy from only 10 sparse measurement locations using only 5 singular vectors

---
Outlook
Test the method with actual satellite measurements such as from the Polar Ozone and Aerosol Measurement (POAM) III instrument
Currently the method is only performed in two dimensions; can it scale to 3-D?
For sources and sinks: if we analyze these from the difference between two retrieved fields, there are at most 2*m degrees of freedom
Eigenvalue decomposition?

---
Outlook
Retrieving sources and sinks:
vec q_N = A_N cdot (A_{N-1} cdot (A_{N-2} cdot (... cdot (A_3 cdot (A_2 cdot A_1 cdot q_0 + %SIGMA_{N-1}) + %SIGMA_{N-2}) + ... %SIGMA_3) + %SIGMA_2) + %SIGMA_1) newline ~= H_N cdot %SIGMA_{N-1} + H_{N-1} cdot %SIGMA_{N-2} + ... H_3 cdot %SIGMA_2 + H_2 cdot %SIGMA_1 + H_1 cdot q_0
Where Si is the source term at time i

---
References
Allen, DR and N Nakamura (2003). “Tracer Equivalent Latitude: A Diagnostic Tool for Isentropic Transport Studies.” Journal of the Atmospheric Sciences, 60: 287-303.
Ott, E (1993) Chaos in Dynamical Systems. Cambridge University Press.
Press, WH, SA Teukolsky, WT Vetterling and BP Flannery (1992). Numerical Recipes in C, 2nd ed. Cambridge University Press.
Randal, CE et al. (2002). “Reconstruction of three-dimensional ozone fields using POAM III during SOLVE.” Journal of Geophysical Research 107 (D20): 8299-8312.
Tang, Y, R Kleeman and S Miller (2006) “ENSO Predictability of a Fully Coupled GCM Model Using Singular Vector Analysis.” Journal of Climate 19 (14): 3361-3377.